## Slide 1: (Prof.) D.K.MEHTA, ASSISTANT PROFESSOR,
CHEMICAL ENGINEERING DEPARTMENT,
L.E.COLLEGE-MORBI

## Slide 2
TOPIC:- INTRODUCTION AND CLASSIFICATION OF MASS TRANSFER OPERATIONS
SUBJECT:-Mass Transfer Operation-I
SUBJECT CODE:-3150501

## Slide 3: 3150501- MASS TRANSFER OPERATION-I
The unit operations involve changes in composition of solutions are known mass transfer operations.
The mass-transfer operations are characterized by transfer of a substance through another on a molecular scale.
It is a very slow molecular diffusive movement.

## Slide 4: Direct contact of two immiscible phases
(1)Gas-Gas
(2)Gas-Liquid
(3)Gas- Solid
(4)Liquid-Liquid
(5)Liquid- Solid
(6)Solid- Solid

## Slide 5: (1)Gas-Gas
Since with very few exceptions all gases are completely soluble in each other, this category is not practically realized.

## Slide 6: (2)Gas-Liquid
Distillation :- All components of the system distribute between the phases at equilibrium. e.g., fractional distillation of petroleum.
Gas Absorption:- Both phases are solution but only one component which distribute between phases. e.g., air-ammonia separation by water.
Humidification:- Liquid phase is pure liquid and gas phase contains two or more components. e.g., humidification of air

## Slide 7: (3) Gas-Solid
Sublimation:- Solid solution is partially vaporize without the appearance of a liquid phase.
Drying:- If a moistened solid is exposed to relatively dry gas, the liquid diffuses into the gas. e.g., drying laundry.
Adsorption:- If a gas mixture brings in contact with solid one or more component of gas mixture diffuses into the solids e.g., adsorption of water vapor from air into activated silica gel

## Slide 8: (4) Liquid-Liquid
Extraction:- It involves separation of a liquid solution with the contact of another insoluble liquid. e.g., separation of acetone- water solution by carbon tetrachloride.

## Slide 9: (5) Liquid-Solid
Crystallization:- Formation of solid particles within a homogeneous phase.
Leaching:- Selective solution of a component from a solid mixture by a liquid solvent is known as leaching. e.g., leaching of gold from its ores by cyanide solutions.
Adsorption:- If a liquid mixture brings in contact with solid one or more component of liquid mixture diffuses into the solids e.g., removal of colored material from sugar solution by activated carbon.

## Slide 10: (6) Solid-Solid
Because of the extra ordinarily slow rates of diffusion within solid phases, there is no industrial separation operation in this category.